## Slide 1: Introducing FGT400D

## Slide 2: FortiGate 400D
2x GE RJ45 Management Ports
8x GE SFP Slots
8x GE RJ45 Ports
Hardware Performance |  |  | 
Firewall Throughput (1518/512/64) | 16/16/16 Gbps | IPS Throughput | 2.8 Gbps
Firewall Latency | 3 μs | Antivirus Throughput (Proxy Based / Flow Based) | 1.4 Gbps
Concurrent Sessions | 5.5 Mil | Virtual Domains (Default / Max) | 10/10
New Sessions/Sec | 200,000 | Max Number of FortiAPs (Total/Tunnel) | 512 / 256
Firewall Policies | 10,000 | Max Number of FortiTokens | 1,000
IPSec VPN Throughput | 14 Gbps | Client-to-Gateway IPSec VPN Tunnels | 10,000
SSL-VPN Throughput | 350 Mbps | Concurrent SSL-VPN Users (Recommended Max) | 500
1
2
3
1
3
2

## Slide 3: FortiGate 400D Schematic
RAM
8GB
Intel Core i7
1G
1G
Ser
Console
2 x 1G Management
RJ45
RJ45
1G
RJ45
RJ45
1G
1G
1G
8x SFP GE
USB
USB
CP8
CP8
Flash
16GB
USB
Dual Core
CPU
SFP
SFP
1G
SFP
SFP
1G
1G
1G
8x GE RJ45
AC PSU
External RPS Connector
FRPS-100
RJ45
RJ45
1G
RJ45
RJ45
1G
1G
1G
SFP
SFP
1G
SFP
SFP
1G
1G
1G
NP6
Notes: 3